SECTION 061053

WOOD NAILERS AND BLOCKING

USE THIS SECTION FOR ROOFING PROJECTS ONLY WHEN SECTION 061000 IS NOT OTHERWISE REQUIRED.

PART 1   GENERAL

1.01	RELATED WORK SPECIFIED ELSEWHERE

EDIT PARAGRAPHS BELOW.

A.	Built-Up Bituminous Roofing System:  Section 075100.

B.	SBS Modified Bitumen Roofing System:  Section 075216.

C.	EPDM Sheet Roofing System:  Section 075323.

D.	Adhered PVC Roofing System:  Section 075419.

1.02	QUALITY ASSURANCE

A.	Mill and Producer’s Stamp:  Each piece of lumber shall bear a stamp indicating type, grade, mill, and grading agency.

USE THIS PARAGRAPH BELOW WHEN SPECIFYING PRESSURE TREATED LUMBER.

1.	Pressure treated wood shall bear a stamp or tag indicating the name of the treating company, year treated, preservative used, the level of treatment, intended use (appropriate AWPA Standard), and logo of inspecting company.

1.03	STORAGE

A.	Store lumber a minimum of 6 inches off the ground, in a dry, well-ventilated place, protected from the weather.

PART 2   PRODUCTS

2.01	MATERIALS

A.	Lumber:  “Standard” Grade Douglas Fir, Hem-Fir, White Pine, Southern Pine, or Spruce-Pine-Fir pressure preservative treated in accordance with the American Wood Preservers Association (AWPA) Standard U1, Commodity Specification A for the requirements listed under Use Category UC2 and kiln dried to 19 percent moisture content after treatment.

USE SUBPARAGRAPH BELOW WHEN FIRE PROTECTION IS REQUIRED.

1.	Use Category UCFA and UCFB:  Wood nailers and blocking intended for fire protection and is used in either interior weather protected (UCFA) or exterior construction, exposed to weather (UCFB).

B.	Nails, Screws, and Bolts:  ASTM A653 Class G185 hot dipped galvanized, zinc or cadmium plated, or silicon bronze.

FASTENERS SPECIFIED IN SUBPARAGRAPH BELOW ARE MORE EXPENSIVE BUT RECOMMENDED.

1.	Screws and Bolts for fastening to Aluminum:  Stainless steel, Type 304 or 316.

FASTENERS SPECIFIED IN PARAGRAPH BELOW ALSO AVAILABLE IN CARBON STEEL AND STAINLESS STEEL.

C.	Expansion Anchors:  G185 Hot dipped galvanized steel wedge anchors, FS FF-S-325, Group II, Type 4, Class 1.

D.	Toggle Bolts:  Cadmium or zinc plated tumble - wing type; FS FF-B-588.

FASTENERS SPECIFIED IN PARAGRAPH BELOW ARE SUITED FOR FASTENING TO ALL TYPES OF MASONRY.

E.	Self Threading Masonry Screws:  Zinc Plated; “Tapcon” by Elco Industries, Inc., 1111 Samuelson Rd., PO Box 7009, Rockford, IL 61125-7009, (815) 397-5151.

PARAGRAPH BELOW IS REQUIRED TO SEPARATE ALUMINUM FLASHINGS, GRAVEL STOPS, COPINGS, JOIST HANGERS, ETC. FROM PRESSURE TREATED WOOD.  WHEN POSSIBLE, DETAIL THE ROOF MEMBRANE BEING USED OVER THE PRESSURE TREATED WOOD BLOCKING – HORIZONTALLY AND VERTICALLY.  SPECIFY THE MEMBRANE TO COVER WOOD BLOCKING AND NAILERS IN PART 3 OF THE ROOFING SECTION AND DELETE BELOW.

F.	Separation Membrane For Aluminum Metals:  Self adhering, self sealing, rubberized asphalt sheet membrane.

1.	Physical Properties:

a.	Thickness:  40 mils minimum ASTM D 3767 Method A.

b.	Tensil strength:  250 psi ASTM D 412.

c.	Elongation (ultimate failure of the rubberized asphalt) 250% ASTM D 412 Die C Modified).

d.	Permeance:  0.05 Perms max.) ASTM E 96.

2.	“Ice And Water Shield” by W.R. Grace Co., 62 Whittemore Ave., Cambridge, MA 02140, (800) 354-5414; “Deck Guard” by Polyguard Products Inc., P.O. Box 755, Ennis, TX 75120, (800) 541-4994; “MetalSeal” by NEI Advanced Composite Technology, 50 Pine Road, Brentwood, NH, (800) 998-4634.

PART 3   EXECUTION

3.01	INSTALLATION

A.	Install nailers and blocking true to line and plane within a tolerance of 1/8 inch in 10 feet.

B.	Fit joints neatly with no more than 1/16 inch space between abutting members.

C.	Do not install nailers or blocking across bonding expansion joints.

D.	Attach nailers and blocking securely as required to properly support the items that will be attached to them.

SIZE, TYPE, LOCATION, AND SPACING OF FASTENERS SHOULD BE INDICATED ON DRAWINGS.  IF THEY ARE NOT, INCLUDE PARAGRAPH BELOW AND APPROPRIATE SUB-PARAGRAPHS.  EDIT AS REQUIRED.

E.	Space fasteners equally at not more than 16 inches on center and 4 inches from each end of each member, unless noted otherwise.  Secure the nailers and blocking with the following types of fasteners:

1.	To Cast-In-Place Concrete, Solid Concrete Masonry Units, and Brick:  Use expansion anchors or self-threading masonry screws.

2.	To Faces of Hollow Concrete Masonry Units:  Use toggle bolts.

3.	To Tops of Hollow Concrete Masonry Units:  Use anchor bolts extending to course below, embedded in 3000 psi concrete filled cores.

4.	To Wood:  Use nails or screws.

5.	To Metal:  Use bolts or self-tapping screws.

F.	Countersink fasteners if they interfere with the proper installation of items to be attached to the nailers and blocking.

DELETE ARTICLE BELOW IF SEPARATION MEMBRANE IS NOT USED IN PART 2 OF THIS SECTION.

3.02	APPLICATION OF SEPARATION MEMBRANE

A.	Installing Separation Membrane:

1.	Install 1 ply of underlayment over the entire horizontal and vertical surface of pressure treated wood nailers and blocking lapping each ply 2 inches over the preceding ply so that no aluminum material comes in contact with pressure treated wood.

END OF SECTION

THE REMAINDER OF THIS DOCUMENT IS FOR INFORMATION ONLY; NOT TO BE INCLUDED IN THE PROJECT SPECIFICATIONS:

Background:

For many years, the most common pressure treating wood preservative for building materials was Chromated Copper Arsenate (CCA).  Starting in early 2004, the pressure treated wood industry ceased producing CCA treated wood for many uses.  A number of new treatments have been developed including Copper Azole (CA), Alkaline Copper Quaternary (ACQ) and Sodium Borate (SBX).  ACQ and CA will be the most likely used preservatives used for building construction.

Some of these new preservatives are significantly more corrosive to metal than was the CCA preservative, due to the higher copper content used.  It is very important to specify and obtain appropriate corrosion resistant materials to ensure adequate service life for fasteners, connectors, hangers, flashings, cladding, etc. that are in contact with the wood.

END OF INFORMATION